## Slide 1
CAPSULE TRACKER
Child Safety & Off-Grid Telemetry System
Real-Time Tracking, Vitals Monitoring, Geofencing & Instant Emergency Alerts
🟢 System Status: Full Ingestion Engine Operational

## Slide 2
OVERVIEW & INFRASTRUCTURE
System Architecture & Core Technology Stack
📡 Hardware Layer
• LoRa Off-Grid Radio Transmission
• Smart Wristband Wearable Unit
• Continuous Pulse & SpO2 Sensors
• Physical SOS Emergency Trigger
• Optical Strap Tamper Sensor
⚙️ Backend Pipeline
• Apache / XAMPP Local Server
• PHP 8 RESTful Telemetry APIs
• PDO Secure MySQL Integration
• Haversine Geofence Engine
• Automated Alert Generator
💻 Dashboard & UI
• HTML5 / CSS3 Responsive Layout
• JavaScript Async Polling (3s Engine)
• Google Maps Dark Theme Styling
• Live Vitals Dashboard Cards
• Dynamic Status Alert Badges

## Slide 3
DATA ENGINE & PERSISTENCE
Database Architecture & Live Ingestion
📊 `telemetry_logs` Table Structure
• latitude & longitude: DECIMAL(10,8) for precise GPS location
• speed: FLOAT for movement velocity tracking
• battery_level: INT percentage of wearable power
• heart_rate & spo2: INT real-time health telemetry
• tamper_status: TINYINT boolean optical strap state
• sos_active: TINYINT instant panic button trigger
🚨 Automated Geofence & Alert Processing
• Haversine Formula Execution: Evaluates distance against preset safe zone center point.
• Geofence Breach Detection: Automatically generates an alert if distance exceeds boundary.
• Tamper Ingestion: Detects strap removal or cut within milliseconds of arrival.
• Unresolved Incident Queue: Stores active alerts in `alert_logs` for instant dashboard broadcast.

## Slide 4
FRONTEND & CONTROLS
Live Monitoring Dashboard & Hardware Simulator
🖥️ Live Safety Dashboard
• Google Maps Dark Mode: Smooth marker repositioning and dynamic map panning.
• Automated 3-Second Poller: Queries `get_dashboard_data.php` seamlessly without full page refresh.
• Real-Time Vitals Display: Heart Rate (BPM), SpO2 (%), Battery Level, and Coordinates.
• Dynamic Status Badge: Color-shifts automatically to RED on SOS emergency or TAMPER breach.
🛠️ Wearable Telemetry Simulator
• Custom Coordinates Test: Test out-of-bounds geofence breaches instantly.
• Biometric Sliders: Simulate spikes in Heart Rate or drop in SpO2.
• Tamper & SOS Controls: Switch states to trigger immediate real-time database alerts.
• JSON Payload Inspector: Displays real-time API response from `receive_telemetry.php`.

## Slide 5
MILESTONES & FUTURE SCOPE
Current Progress & Development Roadmap
✅ Completed Achievements
✓ MySQL relational database schema designed and normalized
✓ Haversine geofencing & backend telemetry ingestion pipeline built
✓ Hardware simulation engine fully functional
✓ Live dashboard integrated with Google Maps dark mode & polling API
✓ Real-time visual alert system operational
🚀 Upcoming Modules
→ Interactive Geofence Zone Management UI (Geofencing.html)
→ Historical Movement Trail & Breadcrumb Playback (Tracking_History.html)
→ Device Configuration & Threshold Settings Page (Setting.html)
→ Physical LoRa SX1278 hardware integration with Arduino/ESP32