## Slide 1
CAPSULE TRACKER
Child Safety & Off-Grid Telemetry System
Real-Time GPS Tracking, Biometric Vitals Monitoring & Instant Tamper Alerts
🟢 Status: Live Backend Ingestion & Dashboard Operational

## Slide 2
BACKGROUND & CHALLENGE
Problem Statement & Project Motivation
⚠️ Existing Safety Limitations
• Cellular Dependence: Standard GPS trackers fail entirely in remote or off-grid areas without SIM signal.
• No Removal Detection: Traditional wearables provide no alert when unbuckled or forcibly cut.
• Lack of Vitals Context: Basic location trackers fail to capture stress signals like elevated heart rates.
💡 The Capsule Tracker Solution
• Long-Range LoRa Mesh: Transmits telemetry parameters up to several kilometers without cellular networks.
• Optical Strap Tamper Sensor: Triggers instantaneous alerts if the wristband is opened.
• Integrated Biometrics: Monitors real-time Heart Rate (BPM) and Blood Oxygen (SpO2).
• Automated Geofence: Instantly flags out-of-bounds occurrences via backend algorithms.

## Slide 3
SYSTEM TOPOLOGY
High-Level System Architecture
🖼️ SYSTEM ARCHITECTURE DIAGRAM
🔄 End-to-End Data Pipeline
1. Smart Wristband Node: Captures GPS coordinates, heart rate, SpO2, SOS button state, and optical tamper status.
2. LoRa Telemetry Transmission: Packets are broadcast over long-range radio frequencies to the central gateway.
3. PHP REST Ingestion Engine: `receive_telemetry.php` receives JSON payloads, executes validation, and processes geofencing.
4. MySQL Relational Storage: Ingested telemetry is committed to normalized SQL tables (`telemetry_logs` & `alert_logs`).
5. Async Live Dashboard: AJAX long-polling updates Google Maps Dark Mode UI every 3 seconds.

## Slide 4
WEARABLE LAYER
Smart Wristband Hardware & Sensor Suite
🎛️ On-Board Components
• LoRa SX1278 Transceiver: 433/868MHz frequency band for long-range transmission.
• GPS Module (NEO-6M): High-precision coordinate positioning.
• PPG Pulse Sensor (MAX30102): Real-time optical heart rate and SpO2 calculation.
• Optical Strap Sensor: Detects physical circuit broken / removal status.
• Panic Button (SOS): Tactile switch triggering immediate high-priority override alerts.
🖼️ WRISTBAND HARDWARE SCHEMATIC

## Slide 5
DATA STORAGE & INGESTION
Relational Database Schema (MySQL)
📋 `telemetry_logs` Schema
• id: INT AUTO_INCREMENT PRIMARY KEY
• device_id: VARCHAR(50) DEFAULT 'WRISTBAND_01'
• latitude & longitude: DECIMAL(10,8) / (11,8)
• speed: FLOAT (Movement tracking)
• battery_level: INT (0-100%)
• heart_rate & spo2: INT (Biometric values)
• tamper_status & sos_active: TINYINT(1)
• created_at: TIMESTAMP DEFAULT CURRENT_TIMESTAMP
🚨 `alert_logs` Schema
• id: INT AUTO_INCREMENT PRIMARY KEY
• device_id: VARCHAR(50) NOT NULL
• alert_type: VARCHAR(50) ('GEOFENCE_BREACH', 'STRAP_TAMPER', 'SOS_EMERGENCY')
• message: TEXT (Detailed emergency description)
• latitude & longitude: DECIMAL(10,8) / (11,8)
• is_resolved: TINYINT(1) DEFAULT 0
• created_at: TIMESTAMP DEFAULT CURRENT_TIMESTAMP

## Slide 6
ALGORITHMIC LOGIC
Real-Time Geofencing Engine
📐 Haversine Distance Formula
Calculates exact great-circle distance between two points on a sphere:
• Δlat = lat2 - lat1 | Δlon = lon2 - lon1
• a = sin²(Δlat/2) + cos(lat1)·cos(lat2)·sin²(Δlon/2)
• c = 2 · atan2( √a, √(1−a) )
• Distance = R · c (where R = 6,371,000 meters)
🛡️ Safe Zone Enforcement
• Dynamic Radius Boundary: Preset home/school center point with configurable safe radius (e.g., 500m).
• Automated Breach Detection: Evaluates incoming coordinates against safe boundary during telemetry parsing.
• Instant Alert Dispatch: Automatically logs 'GEOFENCE_BREACH' entry into `alert_logs` if computed distance exceeds radius.

## Slide 7
SECURITY & PROTECTION
Emergency & Tamper Alert Ingestion
Real-Time Threat Handling
• Strap Tamper Trigger: Instant detection when the optical circuit opens. `receive_telemetry.php` immediately logs 'STRAP_TAMPER'.
• Panic SOS Trigger: Manual activation by child creates high-priority 'SOS_EMERGENCY' alert.
• Visual UI Override: Flashes red emergency badge on the frontend monitoring system.
• Unresolved Alert Queue: Persists warning state until administrator clears the event.
🖼️ ALERT BADGE OVERRIDE SCREENSHOT

## Slide 8
FRONTEND DASHBOARD
Web Control Center & Interactive Map
🖼️ LIVE DASHBOARD SCREENSHOT (INDEX.HTML)
Dashboard Interface
("index.html")
• Google Maps Dark Mode: High contrast, dark styled vector map centered on live coordinates.
• Async 3-Second Poller: `fetchDashboardData()` retrieves telemetry smooth without page reloads.
• Biometric Cards: Live Heart Rate (BPM), SpO2 (%), and Wearable Battery percentage.
• Quick Emergency Controls: Ping Wristband transmitter and Remote Alarm Siren trigger.

## Slide 9
TESTING & EMULATION
Hardware Telemetry Simulator Environment
🛠️ Telemetry Simulator (`simulator.html`)
• Coordinate Manipulation: Test custom GPS points to simulate geofence boundaries.
• Biometric Sliders: Dynamic adjustment of simulated Heart Rate (BPM) and SpO2 levels.
• Hardware State Toggles: Instantly force SOS Active or Strap Cut states.
• API Response Console: Displays real-time JSON responses returned by PHP scripts.
🖼️ SIMULATOR UI SCREENSHOT (SIMULATOR.HTML)

## Slide 10
PHP API ARCHITECTURE
RESTful Backend API Infrastructure
receive_telemetry.php
• Method: POST (JSON Payload Ingestion)
• Validates input payload fields and checks bounds.
• Executes Haversine Geofence comparison.
• Inserts packet into `telemetry_logs`.
• Generates emergency alerts in `alert_logs` if tamper or SOS active.
get_dashboard_data.php
• Method: GET (JSON Response)
• Queries latest record from `telemetry_logs`.
• Fetches active unresolved warnings from `alert_logs`.
• Returns synchronized JSON telemetry state to dashboard JS engine.

## Slide 11
DEBUGGING & OPTIMIZATION
Technical Challenges & Solutions Resolved
Engineering Resolutions
• Database Column Mismatch (SQL State 42S22): Resolved missing 'device_id' column issue in `alert_logs` table via automated migration scripts.
• Async Dynamic Map Polling: Replaced static random telemetry simulation in JS with an active 3-second fetch engine connected to `get_dashboard_data.php`.
• Google Maps Marker Repositioning: Implemented smooth `panTo()` map re-centering without full iframe/DOM re-renders.
• Visual Alert Badge Override: Configured conditional CSS logic to switch status badges dynamically based on backend SOS/Tamper flags.

## Slide 12
PROJECT PHASING
Development Roadmap & Future Expansion
Phase 1: Completed
✓ MySQL database schema & connection setup
✓ Haversine geofencing & backend telemetry ingestion API
✓ Interactive telemetry simulator interface
✓ Live dark-mode dashboard with async polling
✓ Real-time visual alert system
Phase 2: Next Steps
→ Geofence UI Configuration (`Geofencing.html`)
→ Historical Breadcrumb Route Playback (`Tracking_History.html`)
→ Device & Threshold Settings UI (`Setting.html`)
→ Physical LoRa SX1278 ESP32 Hardware Deployment

## Slide 13
EXECUTION PLAN
Live System Demonstration Workflow
🧪 Live Test Procedure
Step 1: Open Live Dashboard (`index.html`) in Primary Window.
Step 2: Launch Telemetry Simulator (`simulator.html`) in Secondary Window.
Step 3: Modify Latitude/Longitude to push device outside safe radius and observe instant Geofence Alert.
Step 4: Toggle Strap Cut / SOS Emergency state in Simulator.
Step 5: Verify automatic MySQL database commit and dynamic UI status badge shift within 3 seconds.

## Slide 14
THANK YOU!
Capsule Tracker: Smart Off-Grid Child Safety & Telemetry
Questions & Demonstration